## Slide 1: Image Detection with RISCV Processor on FPGA
Joshua Wallace
Supervisor: Matthew D’Souza

## Slide 2: Overview Demonstrating how FPGAs can be used to accelerate image processing methods.
01 | Context and Background | 3-7
 | FPGAs, RISC-V, Image Processing, Processing Techniques, Hardware Acceleration | 
02 | Implementation | 8-10
 | Hardware Implementation, Software Implementation, Architecture | 
03 | Progress | 11
04 | Benchmarking | 12
05 | Plan | 13
06 | Challenges | 14
07 | Contact | 15

## Slide 3: FPGAs
Reconfigurability allows for specific algorithms
Parallelised processing for efficient algorithm execution.
Low-latency processing for real-time applications.
Low-power consumption advantage for embedded systems.
Field programmable gate array

## Slide 4: RISC-V
Reduced instruction set architecture
Open-source instruction set architecture (ISA)
Extensible; can have custom instructions
Control over hardware resources for embedded systems
Produces simple, minimal SoC designs

## Slide 5: Image processing
Real-time processing has strict timing constraints
Increasing algorithm complexity and large volumes of data means efficient algorithms are required
Processing methods include:
Segmentation
Edge detection
Object detection
Image classification and more
Retrieving information from an image

## Slide 6: Processing Techniques
Processing extracts features from an image
Edge detection and kernel gradient form the basis of most techniques
Sobel, Prewitt, Canny, Laplacian filter are common edge detection techniques using gradient/gaussian methods
Processing techniques moving in the direction of neural nets (CNNs) via convolution
Types and common techniques

## Slide 7: Hardware acceleration
CPU/MCU can execute sequentially
GPU/FPGA allow for parallel architectures
FPGAs allow for application-specific accelerators which are deterministic: Memory access, threading etc
GPUs are general-purpose parallel computation
Not optimal for big data or deep learning tasks as FPGAs more resource constrained
Leveraging FPGAs for high throughput and low latency

## Slide 8: Software implementation
Using Python and C for software definitions.
On-chip in software vs hardware definitions
CPU programming offloads compute intensive tasks to hardware
Python scripts required to retrieve network parameters
Dedicated hardware components execute algorithms, generally by multiplier accumulator (MAC) units
Notes: Many IO operations, loads. Software is simpler

## Slide 9: Hardware implementation
Written for Xilinx Artix 7 Family FPGA (XC7A35TICPG236-1L)
RISC-V softcore processor (NeoRV32)
Processor written in VHDL, connected via Wishbone bus to hardware resources
Methods implemented using DSPs and LUTs
Neurons defined in hardware
Implementing processing algorithms in VHDL

## Slide 10: Architecture and Development
Using Digilent Basys 3 development board.
Input image (640x480 pixels) stored into BRAM from peripheral camera module
FPGA image processing pipeline from camera to VGA output
Processing performed in hardware
Output image / classification written to BRAM
Control processing via FSM to ensure timing

## Slide 11: Progress
Status of the work
NeoRV32 softcore processor with Wishbone B4 interconnect implemented on Basys 3.
Python scripts and notebooks for selected techniques.
Single-layer MNIST CNN trained for classification with weights exported via ONNX from Pytorch.
Generating hardware implementations of a CNN: Neuron, ReLu, Convolution.

## Slide 12: Benchmarking
Testing the performance
Inference time / Execution time
Benchmark performance against common applications
FPGA hardware / software
CPU only
CPU with GPU accelerator
Embedded devices
Detection verified by MSE; classification verified by validation loss / accuracy
Notes: Decrease critical path

## Slide 13
01
RISCV Softcore Processor
  NeoRV32 processor on Basys 3
  Wishbone B4 interconnect
02
Custom Hardware and Software
  Define algorithms in hardware (VHDL)
  Define algorithms in software (Python, C)
03
Peripherals
  Connect pipeline to OVD7670 camera for input
  Display output on VGA monitor
04
Benchmarking
  Integrate and test
  Measure inference times and compare
Plan
Where is the project going?

## Slide 14: Challenges
BRAM resources on Basys 3 is limited for storing and retrieval of image data → Change board
Fixed point arithmetic requires selecting minimal bit widths without loss of accuracy
Resource utilization for defining a convolution layer
Multiplication can be done in LUTs or DSPs
Limited number of DSP slices
Potential issues identified

## Slide 15: Contact
Joshua Wallace
Image Detection with RISCV Processor on FPGA
joshua.wallace1@uq.edu.au